## Slide 1: Study of 8051 microcontroller and its architecture:

## Slide 2
meeting the computing needs of the task efficiently and cost effectively
  speed, the amount of ROM and RAM, the number of I/O ports and timers, size, packaging, power consumption
  easy to upgrade
  cost per unit
availability of software development tools
  assemblers, debuggers, C compilers, emulator, simulator, technical support
wide availability and reliable sources of the microcontrollers.
Three criteria in Choosing a Microcontroller

## Slide 3: The 8051 microcontroller
a Harvard architecture (separate instruction/data memories)
single chip microcontroller (µC)
developed by Intel in 1980 for use in embedded systems.
today largely superseded by a vast range of faster and/or functionally enhanced 8051-compatible devices manufactured by more than 20 independent manufacturers

## Slide 4: Block Diagram
CPU
On-chip RAM
On-chip ROM for program code
4 I/O Ports
Timer 0
Serial Port
OSC
Interrupt Control
External interrupts
Timer 1
Timer/Counter
Bus Control
TxD RxD
P0 P1 P2 P3
Address/Data
Counter Inputs

## Slide 5
Feature 8051 8052 8031
ROM (program space in bytes) 4K 8K 0K
RAM (bytes) 128 256 128
Timers 2 3 2
I/O pins 32 32 32
Serial port 1 1 1
Interrupt sources 6 8 6
Comparison of the 8051 Family Members

## Slide 6: Pin Description of the 8051
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
17
18
19
20
40
39
38
37
36
35
34
33
32
31
30
29
28
27
26
25
24
23
22
21
P1.0
P1.1
P1.2
P1.3
P1.4
P1.5
P1.6
P1.7
RST
(RXD)P3.0
(TXD)P3.1
(T0)P3.4
(T1)P3.5
XTAL2
XTAL1
GND
(INT0)P3.2
(INT1)P3.3
(RD)P3.7
(WR)P3.6
Vcc
P0.0(AD0)
P0.1(AD1)
P0.2(AD2)
P0.3(AD3)
P0.4(AD4)
P0.5(AD5)
P0.6(AD6)
P0.7(AD7)
EA/VPP
ALE/PROG
PSEN
P2.7(A15)
P2.6(A14)
P2.5(A13)
P2.4(A12)
P2.3(A11)
P2.2(A10)
P2.1(A9)
P2.0(A8)
8051
(8031)


## Slide 8: Pins of 8051（1/4）
Vcc（pin 40）：
  Vcc provides supply voltage to the chip.
  The voltage source is +5V.
GND（pin 20）：ground
XTAL1 and XTAL2（pins 19,18）：
  These 2 pins provide external clock.
  Way 1：using a quartz crystal oscillator
  Way 2：using a TTL oscillator
  Example 4-1 shows the relationship between XTAL and the machine cycle.

## Slide 9: Pins of 8051（2/4）
RST（pin 9）：reset
  It is an input pin and is active high（normally low）.
    The high pulse must be high at least 2 machine cycles.
  It is a power-on reset.
    Upon applying a high pulse to RST, the microcontroller will reset and all values in registers will be lost.
    Reset values of some 8051 registers
  Way 1：Power-on reset circuit
  Way 2：Power-on reset with debounce

## Slide 10: Pins of 8051（3/4）
/EA（pin 31）：external access
  There is no on-chip ROM in 8031 and 8032 .
  The /EA pin is connected to GND to indicate the code is stored externally.
  /PSEN ＆ ALE are used for external ROM.
  For 8051, /EA pin is connected to Vcc.
  “/” means active low.
/PSEN（pin 29）：program store enable
  This is an output pin and is connected to the OE pin of the ROM.
  See Chapter 14.

## Slide 11: Pins of 8051（4/4）
ALE（pin 30）：address latch enable
  It is an output pin and is active high.
  8051 port 0 provides both address and data.
  The ALE pin is used for de-multiplexing the address and data by connecting to the G pin of the 74LS373 latch.
I/O port pins
  The four ports P0, P1, P2, and P3.
  Each port uses 8 pins.
  All I/O pins are bi-directional.

## Slide 12: Figure 4-2 (a). XTAL Connection to 8051
C2
30pF
C1
30pF
XTAL2
XTAL1
GND
Using a quartz crystal oscillator
We can observe the frequency on the XTAL2 pin.


## Slide 13: Figure 4-2 (b). XTAL Connection to an External Clock Source
NC
EXTERNAL
OSCILLATOR
SIGNAL
XTAL2
XTAL1
GND
Using a TTL oscillator
XTAL2 is unconnected.


## Slide 14: RESET Value of Some 8051 Registers:
0000
DPTR
0007
SP
0000
PSW
0000
B
0000
ACC
0000
PC
Reset Value
Register
RAM are all zero.


## Slide 15: Figure 4-3 (a). Power-On RESET Circuit
30 pF
30 pF
8.2 K
10 uF
+
Vcc
11.0592 MHz
EA/VPP
X1
X2
RST
31
19
18
9


## Slide 16: Figure 4-3 (b). Power-On RESET with Debounce
EA/VPP
X1
X2
RST
Vcc
10 uF
8.2 K
30 pF
9
31


## Slide 17: Pins of I/O Port
The 8051 has four I/O ports
  Port 0 （pins 32-39）：P0（P0.0～P0.7）
  Port 1（pins 1-8） ：P1（P1.0～P1.7）
  Port 2（pins 21-28）：P2（P2.0～P2.7）
  Port 3（pins 10-17）：P3（P3.0～P3.7）
  Each port has 8 pins.
    Named P0.X （X=0,1,...,7）, P1.X, P2.X, P3.X
    Ex：P0.0 is the bit 0（LSB）of P0
    Ex：P0.7 is the bit 7（MSB）of P0
    These 8 bits form a byte.
Each port can be used as input or output (bi-direction).

Notes: Program is to read data from P0 and then send data to P1

## Slide 18
Registers
A
B
R0
R1
R3
R4
R2
R5
R7
R6
DPH
DPL
PC
DPTR
PC
Some 8051 16-bit Register
Some 8-bitt Registers of the 8051

## Slide 19: Memory Map (RAM)

## Slide 20: CPU timing
Most 8051 instructions are executed in one cycle.
MUL (multiply) and DIV (divide) are the only
instructions that take more than two cycles to complete (four cycles)
Normally two code bytes are fetched from the program memory during every machine cycle.
The only exception to this is when a MOVX instruction is executed. MOVX is a one-byte, 2-cycle instruction that accesses external data memory.
During a MOVX, the two fetches in the second cycle are skipped while the external data memory is being addressed and strobed.

## Slide 21: 8051 machine cycle

## Slide 22: Example :

Find the machine cycle for
(a) XTAL = 11.0592 MHz
(b) XTAL = 16 MHz.
Solution:
(a) 11.0592 MHz / 12 = 921.6 kHz;
machine cycle = 1 / 921.6 kHz = 1.085 s
(b) 16 MHz / 12 = 1.333 MHz;
machine cycle = 1 / 1.333 MHz = 0.75 s

## Slide 23: Edsim51 emulator diagram

## Slide 24: KitCON-515 schematic

## Slide 25: Timers
8051 has two 16-bit on-chip timers that can be used for timing durations or for counting external events
The high byte for timer 1 (TH1) is at address 8DH while the low byte (TL1) is at 8BH
The high byte for timer 0 (TH0) is at 8CH while the low byte (TL0) is at 8AH.
Timer Mode Register (TMOD) is at address 88H

## Slide 26: Timer Mode Register
Bit 7: Gate bit; when set, timer only runs while \INT high. (T0)
Bit 6: Counter/timer select bit; when set timer is an event counter when cleared timer is an interval timer (T0)
Bit 5: Mode bit 1 (T0)
Bit 4: Mode bit 0 (T0)
Bit 3: Gate bit; when set, timer only runs while \INT high. (T1)
Bit 2: Counter/timer select bit; when set timer is an event counter when cleared timer is an interval timer (T1)
Bit 1: Mode bit 1 (T1)
Bit 0: Mode bit 0 (T1)

## Slide 27: Timer Modes
M1-M0: 00 (Mode 0) – 13-bit mode (not commonly used)
M1-M0: 01 (Mode 1) - 16-bit timer mode
M1-M0: 10 (Mode 2) - 8-bit auto-reload mode
M1-M0: 11 (Mode 3) – Split timer mode

## Slide 28: 8051 Interrupt Vector Table

## Slide 29: The Stack and Stack Pointer
The Stack Pointer, like all registers except DPTR and PC, may hold an 8-bit (1-byte) value.
The Stack Pointer is used to indicate where the next value to be removed from the stack should be taken from.
When you push a value onto the stack, the 8051 first increments the value of SP and then stores the value at the resulting memory location.
When you pop a value off the stack, the 8051 returns the value from the memory location indicated by SP, and then decrements the value of SP.
This order of operation is important. When the 8051 is initialized SP will be initialized to 07h. If you immediately push a value onto the stack, the value will be stored in Internal RAM address 08h. This makes sense taking into account what was mentioned two paragraphs above: First the 8051 will increment the value of SP (from 07h to 08h) and then will store the pushed value at that memory address (08h).
SP is modified directly by the 8051 by six instructions: PUSH, POP, ACALL, LCALL, RET, and RETI. It is also used intrinsically whenever an interrupt is triggered