Real Time Protocol
Sagar Giri

---
Introduction
- RTP is a data transport protocol for real-time application.
- RTCP is a control protocol accompanying RTP.
- RTP is designed to support multicast communication in interactive multimedia applications, such as audio/ video teleconferencing and distributed simulation.
- It deals solely with data delivery.

---
Introduction
- RTP can run over unreliable protocol UDP.
- It uses UDP's multiplexing and error control services while monitoring, control, and identification functions are provided by RTCP.
- RTP is scalable
- RTP assumes that the multicast group membership can change dynamically.
- RTP runs on top of UDP, so, there is no guarantee against lost and out-of-sequence packets.

---
Architecture
RTP application architecture
Applications
RTP & RTCP
Other transport and network protocols	UDP
	IP

---
RTP Header
Synchronization Source identifier (SSRC)
Miscellaneous fields
Sequence Number
Timestamp
Payload Type
- Payload Type: 7 bits, providing 128 possible different types of encoding; eg JPEG, MPEG2 video, etc. different media are not multiplexed
- Sequence Number: 16 bits; random number incremented by one for each RTP data packet sent; used to detect packet loss

---
RTP Header
Synchronization Source identifier (SSRC)
Miscellaneous fields
Sequence Number
Timestamp
Payload Type
- Timestamp: 32 bytes; gives the sampling instant of the first audio/video byte in the packet; used to remove jitter introduced by the network
  - clock frequency depends on applications
  - random initial value
  - several packets may have equal timestamps (eg. same video frame), or even in disorder (eg. interpolated frames in MPEG)

---
RTP Header
Synchronization Source identifier (SSRC)
Miscellaneous fields
Sequence Number
Timestamp
Payload Type
- Synchronization Source identifier (SSRC) : 32 bits; an id for the source of a stream; assigned randomly by the source
- Miscellaneous fields: Contributing Source identifier (CSRC)

---
Thank You!